Name

Date 		 Pd

### E&M Unit 4 - Magnetism: Worksheet 6

1.	Ben D. Straw runs at 5.0 m/s through a room carrying an upright aluminum rod 40 cm long.  The room happens to have a magnetic field with a strength of 0.5 T, oriented as shown to the right.

- Indicate on the diagram above which end of the rod becomes positive and which end negative.

- What is the change in potential between the ends of the rod?

- What is the strength of the electric field in the rod?

2.  Liz N. Twomey pushes a metal bar to the right at 6.0 m/s.  The bar is sliding along a pair of metal rails that are resting horizontally on the ground.  A magnetic field of 0.20T is oriented out of the page as shown in the diagram to the right.

- At what rate is the flux changing in the loop formed by sliding the bar?

- If the loop has a resistance of 0.50 Ω, what is the current in the loop?  Indicate on the diagram the direction of the current in the loop.

3.  To the right is a 0.40m x 0.50 m rectangular loop in a uniform magnetic field of 0.80 T out of the page as shown on the diagram to the right.

- What is the induced emf for the loop?  Indicate on the diagram to the right the direction of the current in the loop.

- The field is then decreased to zero at a constant rate in 2.0 seconds.  Indicate on the diagram to the right the direction of the current in the loop.

- If the loop has a resistance of 0.10Ω, what is the value for the current in the loop?

4.  To the right is a coil of wire between the ends of a horseshoe magnet with a constant field of 0.6T.  The coil is forced to rotate 4 times per second to generate an emf.  The coil has dimensions 8 cm wide and 10 cm long.

- If you view the coil from below, it is rotating clockwise. (left side toward you, right side away from you from a top perspective)   Is positive charge forced from A to B or B to A or not at all as the loop arrives at this location?  Place a + on the high potential end and a – on the low potential.

- How much flux is there through the loop here?  How much 90 degrees later?

- As the coil rotates through 90 degrees, what is the average emf induced in the coil?

- On the graph below, plot the points for the flux through the coil of wire every 90° using the position in the diagram as 0 degrees.  (Remember that A is rotating.)  +( is the maximum and -( is the minimum, you need not plot actual numbers.  Try to connect between the points.

- On the graph below, plot the points for the emf in the loop every 90°.  + is the maximum and - is the minimum, you need not plot actual numbers.  Try to connect between the points.

- What are two methods by which you make the generator provide higher emf?

5.  To the right is a metal ring of radius 0.30 m with a clockwise current of 600 mA.  The ring has a resistance of 0.20Ω.

- Is the magnetic field strength increasing or decreasing?  Explain your reasoning.

- At what rate is the field changing? (In T/s)

# Text boxes

2.0 m

0.50 m

0.40 m

N

# S

A

B

0

-(

+(

90

180

270

360

0

-

+

90

180

270

360