Name 		Date 		 Period

Waves Unit II, Worksheet 6

- A string is fixed between the wave driver and pulley located 50.0 cm apart.  A 200. g mass is atteched to the end of the string providing the tension.  When a wave generator vibrates at 150. Hz the string resonates in the third mode.

- Sketch the first 5 modes of vibration for this setup

- Find the wavelength for each of these modes

- Determine the speed of the wave for each of these modes

- Determine the resonant frequency for each of these modes

| MODE | DIAGRAM | WAVELENGTH | FREQUENCY | WAVE SPEED |
| --- | --- | --- | --- | --- |
| 1st |  |  |  |  |
| 2nd |  |  |  |  |
| 3rd |  |  | 150. Hz |  |
| 4th |  |  |  |  |
| 5th |  |  |  |  |

- The same string is attached to a hanging mass of 400 g.  The linear density and the length of the string have not changed.

a. Find the linear density for the string.

b. Complete the chart for the first four modes of vibration.

| MODE | DIAGRAM | WAVELENGTH | FREQUENCY | WAVE SPEED |
| --- | --- | --- | --- | --- |
| 1st |  |  |  |  |
| 2nd |  |  |  |  |
| 3rd |  |  |  |  |
| 4th |  |  |  |  |

- Eric Clapton plucks a C on a guitar string, which causes a fundamental frequency of 261 Hz.  The wave travels down the string at 400. m/s.

a.  Draw a picture of the standing wave.  If the linear density of the string is .417g/m, what is the tension on the string?

b.  Determine the wavelength of the wave.

4.	Describe some factors that a guitar player can change to vary the frequency (pitch) of the sound produced by a guitar. Describe the change that each one would produce in the pitch of the sound.  (Hint: you should be able to identify four changes that affect the pitch.)

# Text boxes

50.0 cm

Mass = 200.g

50.0 cm

50.0 cm