Experiment 8: Acceleration Down an Incline

Purpose:

In this experiment, you will investigate how the acceleration of a cart rolling down an inclined track depends on the angle of incline. From you data, you will calculate the acceleration of an object in free-fall.

Theory:

A cart of mass m on an incline will roll down the incline as it is pulled by gravity. The force of gravity (mg) is straight down as shown in Figure 8.1. The component of that is parallel to the inclined surface is mg sin (.

To determine the acceleration, you will release the cart from rest and measure the time (t) for it to travel a certain distance (d). Since d = ½at2, the acceleration can be calculated using a = 2d/t2 .

A plot of a versus sin ( will be a straight line with a slope equal to the acceleration of an object in free-fall, g.

Figure 8.2

Materials:

| Required Equipment from Dynamics System | Stopwatch |
| --- | --- |
| Track with End Stop | Graph paper |
| PAScar | Suggested Model Number |
| Pivot Clamp Other Required Equipment | ME-9355 |
| Base and support rod | ME-1234 |

Procedure:

- Set up the track as shown in Figure 8.2 with a pivot clamp and support stand. Elevate the end of the track by about 10 cm.

- Set the cart on the track against the end stop and record this final position in 
Table 8.1. (Use the non-magnetic end of the cart so it touches the end stop.)

- Pull the cart up to the top of the track and record the initial position where the 
cart will be released from rest.

- Release the cart from rest and use the stopwatch to time how long it takes the cart to reach the end stop. The person who releases the cart should also operate the stopwatch. Repeat this measurement 5 times (with different people doing the timing). Record all the values in Table 8.1.

- Lower the end of the track by I cm and repeat step 4. Use the same release position.

- Repeat step 4 for a total of 7 angles, lowering the end of the track by 1 cm for 
each new angle.

Table 8.1: Data

|  | Initial release position = |  |  |
| --- | --- | --- | --- |
|  | Final position = |  |  |
|  | Distance traveled (d) = |  |  |
|  |  |  | Height of Track |  |  |
|  | 10 cm | 9cm | 8cm | 7cm | 6cm | 5cm | 4cm |
| Time | Trial 1 |  |  |  |  |  |  |  |
|  | Trial 2 |  |  |  |  |  |  |  |
|  | Trial 3 |  |  |  |  |  |  |  |
|  | Trial 4 |  |  |  |  |  |  |  |
|  | Trial 5 |  |  |  |  |  |  |  |
|  | Average |  |  |  |  |  |  |  |

Data Analysis:

- Calculate the average time for each angle and record it in Table 8.1.

- Calculate the distance traveled, d, from the initial to the final position.

- Use the distance traveled and average time to calculate the acceleration for each angle and record it in Table 8.2. If you cannot figure out how to do this, refer to the theory.

Table 8.2: Analysis

| Height | Acceleration |
| --- | --- |
| 10 cm |  |
| 9 cm |  |
| 8 cm |  |
| 7 cm |  |
| 6 cm |  |
| 5 cm |  |
| 4 cm |  |

- Plot acceleration versus height and draw the best-fit straight line.

- Based upon your data, how does the height of the incline relate to the acceleration of the cart?

- If you were capable of increasing the angle to 90o, what do you think the acceleration of the cart would be?

Error Analysis & Conclusion: