Series & Parallel Circuits Lab WS

I.  Series Circuits (Simulation Only)

Use the CCK (Circuit Construction Kit) simulation to build the circuits below with a battery at about 12 volts and light bulbs (represented by the ~ symbol). Turn on the voltmeter and ammeter to measure voltage of the battery and current into it. Complete the data table as shown and record the apparent brightness of the bulb.

| # of bulbs | Battery voltage (v) | Current into battery (A) | Brightness of bulbs |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |

Figure 1		Figure 2		Figure 3

- Summarize the relationships you observed and explain what you think is happening.

- How does changing the battery voltage affect your results?

- Practice using the voltmeter and realistic ammeter in several circuits.  Describe how using a voltmeter is different from using an ammeter.

II. Parallel Circuits (Simulation Only)

Redo Part I but use figures 4-6 for the circuits. Make a new table and answer questions a) and b) above.

Figure 4		Figure 5		Figure 6

III. Actual Resistors

Get a resistor and click the ‘values’ option to find its resistance R (in ohms). Get a battery and measure the voltage. Calculate the current (I) that should run through the circuits when the resistor is hooked up to one, two, or all three batteries.

| Batteries | Total voltage (V) | Resistance (() | Calculated Current (A) |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 1+2 |  |  |  |
| 1+2+3 |  |  |  |

(Continued on next page)

Now build the following circuits in the simulation.  Use the voltmeter and ammeter to get your readings where shown on the diagram (V for voltage, A for current) by changing the mode and moving it.  Voltage is measured across the circuit, and current is measured with the meter in the circuit.  Record your data in a table like the one below.

| Batteries | Measured Voltage (V) | Measured Current (A) |
| --- | --- | --- |
| 1 |  |  |
| 1+2 |  |  |
| 1+2+3 |  |  |

- Explain what might be happening to cause the change in current as batteries are added.

- How are current and battery voltage related? Sketch a graph of current and voltage.

- What does the slope of the current and voltage graph represent?

IV. Variable Resistors

Use a resistor connected to the batter set on 3 volts to make a circuit. Then use the voltmeter and ammeter to read the current and voltage where indicated. Vary the resistance of the resistor by moving the slider.  Make a data table using with at least 10 resistances for the resistor.

- Sketch a graph showing the relationship between resistance and current.

- Is the relationship between current and resistance proportional or inversely proportional?  Please explain your reasoning.

# Text boxes

A

V

A

V

A

V

A

V

DC

DC